## Slide 1: Open JTS – Juniper Telemetry Stack
09/2023 - David Roy – TME MX

## Slide 2: Legal Disclaimer
Juniper may disclose information related to their development and plans for future products, features or enhancements ("SOPD"). SOPD information is subject to change at any time, without notice. Except as may be set forth in definitive agreements for the potential transaction, Juniper provides no assurances, and assumes no responsibility, that future products, features or enhancements will be introduced. Except as may be set forth in definitive agreements for the potential transaction, Company should not base purchasing decisions upon reliance of timeframes or specifics outlined in an SOPD, because Juniper may delay or never introduce the future products, features or enhancements.

## Slide 3
SNMP
Collect mode: PULL
Transport Layer: IP / UDP (not reliable)
Port: 161
Application layer: SNMPv1; v2 or v3
Data model: MIB proprietary or standardized
Data format: SMI / ASN-1
Timestamp: Set by collector
Encoding : BER
Security: Community or key with SNMPv3
TELEMETRY gRPC
Collect mode: PUSH - STREAM
Transport Layer: IP / TCP (reliable)
Port : 9339 (configurable)
Application layer: HTTP/2 gRPC
Data model: Vendor specific or Vendor Neutral
Data format: YANG
Timestamp: Set by the router (even LC)
Encoding : ProtoBuf (GPB) or JSON
Security: login/pwd & TLS certificate
Why Telemetry ?
AND LAST BUT NOT THE LEAST
MOST OF THE NEW COUNTERS ARE ONLY AVAILABLE VIA TELEMETRY

## Slide 4: Juniper supports many sensors…
Segment
Routing
SENSOR
BGP
SENSOR
IGP
SENSOR
RSVP
SENSOR
PFE
SENSOR
Hardware
SENSOR
Chassis inventory
SENSOR
BNG
SENSOR
Fabric
SENSOR
OTN
SENSOR
NPU
SENSOR
AND MANY OTHERS
SENSOR
Power Usage
SENSOR
Visit: https://apps.juniper.net/ydm-explorer/

## Slide 5: Juniper Initiative Help our customers to discover the power of the Juniper Streaming Telemetry
A Reboot of the OpenNTI Opensource project but with more features:
Provide a complete/integrated/simple solution to quickly discover/test the power of Juniper Telemetry Interface
Build around several OpenSource Tools and some Juniper development.
For lab/pre-production
Help discovering Juniper Telemetry Power for the routing portofolio: ACX, MX, PTX and probably more in a second phase
Deploy in one command: Telemetry up and running in few minutes - easy to use!
Shipped with pre-defined templates and dashbords: nothing to do!
Easy to evolve – New profiles will be added during the time
New Code Name for this OpenSource initiative:
OpenJTS
Juniper Telemetry Stack

## Slide 6: OpenJTS Architecture
90% OpenSource Tools
10% Juniper dev.

## Slide 7: JTS Enricher
Automatic Enricher base on Netconf
Collect well-known « show » command
Format output in JSON files that will be injested by the Telemetry collectors: help to enrich on-the-fly telemetry data. JSON file maybe also modified with additionnal data by third party tool.
GNMI
Input Plugin
KPI
Rename Plugin
Enricher
Plugin
Output Influxdb Plugin
To DB
TELEGRAF (Telemetry Collector)
Auto-Generated by the JTS ENRICHER
From Routers
Timestamp: 2023-10-18T09:09:25.12Z
Tags:
if_name: et-1/0/0
device: londonr01
Fields:
in_octets = 1500515
out_octets = 1544156165
Timestamp: 2023-10-18T09:09:25.12Z
Tags:
if_name: et-1/0/0
device: londonr01
PEER: parisr02
TYPE: core_interface
MODEL: MX480
VERSION: 23.2R1.15
POP: LONDON
Fields:
in_octets = 1500515
out_octets = 1544156165
Juniper
Dev.

## Slide 8: JTS Profile What is a profile?
myname.tgz
definition.json
Collector config files
(telegraf)
Collector config files
(telegraf)
Collector config files
(Telegraf)
Collector config files
(telegraf)
Collector config files
(telegraf)
Tick Scripts
(Kapacitor)
Collector config files
(telegraf)
Collector config files
(telegraf)
Dashboard
(Grafana)
definition.json
Just a TGZ file including several files.
Must follow naming convention
Design Guide to let anybody make his own profile will be provided.
Easy to evolve… Adding profiles without touching the code…

## Slide 9: OpenJTS up and running
Steps to play with OpenJTS:
  Enable gRPC and Netconf services
  git clone https://xxxxxxxx/jts
  docker compose up -d
  Go to http://xxxxx/jtso.html
    Fill your routers IP/Name/Credentials info
    Assign a pre-defined profile to your routers:
      Optical monitoring profile
      Health monitoring profile
      Traffic & CoS monitoring profile
      BGP monitoring profile
      …
  Use pre-shipped Grafana Dashboard
  Enjoy your KPI and That’s all….

## Slide 10
# Netconf User
set system login user netconf_user class super-user
set system login user netconf_user authentication encrypted-password “”
#gNMI User
set system login user gnmi_user class super-user
set system login user gnmi_user authentication encrypted-password “”
# Clear Text gRPC
set system services extension-service request-response grpc clear-text port 9339
set system services extension-service request-response grpc max-connections 8
set system services extension-service request-response grpc skip-authentication
# Or TLS encryption gRPC
set system services extension-service request-response grpc ssl port 9339
set system services extension-service request-response grpc ssl local-certificate lcert
set system services extension-service request-response grpc ssl mutual-authentication certificate-authority ca1
set system services extension-service request-response grpc ssl mutual-authentication client-certificate-request require-certificate-and-verify
# Netconf
set system services netconf ssh
set system services netconf rfc-compliant #optional
Simple User Guide Step 1: configure your router(s) - do it only one time

## Slide 11
dave@ubuntu-02:~$ mkdir -p /opt/JTS
dave@ubuntu-02:$ cd /opt/JTS
dave@ubuntu-02:/opt/JTS$ git clone https://door7302@xxxxxxxxxxxxxxxxx/jts.git .
dave@ubuntu-02:/opt/JTS$ cd compose
dave@ubuntu-02:/opt/JTS/compose$ docker compose up –d
[+] Running 8/8
✔ Network compose_default Created
✔ Container influxdb Started
✔ Container jtso Started
✔ Container grafana Started
✔ Container kapacitor Started
✔ Container telegraf_ptx Started
✔ Container telegraf_mx Started
✔ Container telegraf_acx Started
Simple User Guide Step 2: Install & Run the stack
First Time it takes 5 minutes due to Telegraf & JTSO compilation
Then it takes 5 seconds to start
Tunning available in the install guide
Do it only one time

## Slide 12
Simple User Guide Step 3: Configure JTSO – Stack state
HTTP & HTTPS Access

## Slide 13
Simple User Guide Step 3: Configure JTSO – Set your credentials - gRPC encryption

## Slide 14
Simple User Guide Step 3: Configure JTSO – Add router(s) to inventory
Auto discovery (Netconf) of the family, model and version

## Slide 15
Simple User Guide Step 4: Access to profile doc

## Slide 16
Simple User Guide Step 5: Assign router(s) to profile(s)
Stack is automatically reconfigured – collect started/stopped

## Slide 17
Simple User Guide Step 6: Access to Grafana Home
HTTP & HTTPS Access
Dynamically updated depending on the active profile(s)

## Slide 18
Simple User Guide Step 7: Enjoy pre-shipped Dahboards